## Slide 1: Tools for In-site Measurement Radio Interference Campaigns for P1451.5p
Jing Geng
Oct 17, 2022

## Slide 2: Time-Sensitive Networking in Industrial Wireless Applications
Rick Candell Industrial Wireless Systems Smart Connected Systems Division
IECON 2022, Brussels

## Slide 3: Requirements for the Spectrum Detector

## Slide 4: Meta Data File :
Requirements for the Spectrum Detector
Detection Event File :

## Slide 5: Wireless Event Capturing Approach
  Basic spectrum analysis :
    Sweep through certain spectrum band, max_hold/average through the capture trace
  Interference hunting through spectrum device :
    Device we test on : BB60C spectrum analyzer
      9kHz to 6GHz
      27 MHz max real-time bandwidth
      Max 40M/s sample rate
    Limitation :
      Hardware limitation for event duration under milli-second
Notes: Advantage : large span of bw sweep
Limiation : hardware

## Slide 6: NIST Machine Shop
  A space with large machines (for welding, milling, lathe work, etc), cranes and tools, workbenches, computers.
  Outer dimensions of approximately 12 m x 15 m (40 ft x 50 ft) and a ceiling height of approximately 7.6 m (25 ft)
  Possible sources and interference :
    Wifi aps, PCs
    Personal cell phones
    Wireless control crane
    Machine noice

## Slide 7: Wireless Event Capturing Approach
  IQ data capturing, process, threshold, and write to events :
Sweep over Desire Bandwidth :
Limitation : real-time bandwidth, software speed

## Slide 8: Wireless Event Capturing Approach
  IQ data capturing, process, threshold, and write to events :
Collect data to the memory limit and do post-processing :

## Slide 9: Wireless Event Capturing Approach
  Zero span recording, threshold, write event :
Narrowing down a smaller bandwidth for each capturing.
Sweep and hop around the total band interested
Calculate only the IQ power for each band and do the thresholding.

## Slide 10: Summary
  Basic requirements for the tool for on-site measurement radio interference.
  Different approaches with different limitations.
  The result can help in better knowing the spectrum activities, interference patterns in different capturing environments.
  Cannot replace the basic analysis for existing protocols, devices, and possibilities.
Notes: Advantage : large span of bw sweep
Limiation : hardware