## Slide 1: Tools for On-site Measurement Radio Interference Campaigns for P1451.5p
Jing Geng Industrial Wireless Systems Smart Connected Systems Division

## Slide 2: Requirements for Spectrum Detector
Notes: Hope to measure what activities and interference in the interested spectrum
So we could emulate or recreate in a SDR

## Slide 3: Wireless Event Capturing Approach
  Basic spectrum analysis :
    Sweep through certain spectrum band, max_hold/average through the capture trace
  Interference hunting through spectrum device :
    Device we test on : BB60C spectrum analyzer
      9kHz to 6GHz
      27 MHz max real-time bandwidth
      Max 40M/s sample rate
Notes: Test with bb60c to see the best possible detail it could capture based on this device

## Slide 4: Detection Output from BB60C

## Slide 5: NIST Machine Shop Measuring
  A space with large machines (for welding, milling, lathe work, etc), cranes and tools, workbenches, computers.
  Outer dimensions of approximately 12 m x 15 m (40 ft x 50 ft) and a ceiling height of approximately 7.6 m (25 ft)
  Possible sources and interference :
    Wi-Fi aps, PCs
    Personal cell phones
    Wireless control crane
    Machine noise
Mobile crane

## Slide 6: Limitations
Limitation on min event captured
Unstable event capturing for periodic signals
Hardware limitation (sweep speed)

## Slide 7: Directly IQ Capturing (1)
Sweeping over the interested band with real-time bandwidth.
IQ data capturing, process, threshold, and write to events.
Limitations : (Capturing input 160 MB/s)
Software processing speed
Memory space limitation (~9.2GB per min.)
Solutions :
Software base acceleration (e.g. GPU, better PC)
Hardware solution

## Slide 8: Directly IQ Capturing (2)
  Zero span recording, threshold, write event :
    Narrowing down a smaller bandwidth for each capturing.
    Sweep and hop around the total interested band
    Calculate only the IQ power and do thresholding
    Much faster and can be implemented real time

## Slide 9: Other Requirements
Min event duration
How detail should the measurement be to characterize in different scenarios.
Others?
Notes: 1 Is it necessary to have the detector capable of detecting in such a small event
2 scenarios (like process control scenarios, scenarios with noises with microwaves, or even other wifi network. Different scenarios have different packet size and transmission datarate)
make the requirement for different scenarios based on device capability

## Slide 10: Possible sites :
  NIST (NIST shop, steam plant)
  Concrete plant, LaFargeHolcim – William Miller
  The J. J. Pickle Research Campus (PRC) in Austin – Juan Conchas
  Intel Casper Site – Javier
  Boeing – Michael Greene
  Office in Spain– Inaki
  Small factory in Spain – Inaki
  Outdoor space (Woodyard at paper mild) – Scott McNeil
  Phoenix contact – Justin shade
  GM General motors
  Small-medium sized factories target
  Ford plant

## Slide 11: Summary
  Basic requirements for the tool for on-site measurement radio interference.
  Different approaches with different limitations.
  The result can help in better knowing the spectrum activities, interference patterns in different capturing environments.
  Cannot replace the basic analysis for existing protocols, devices, and possibilities.
Notes: Advantage : large span of bw sweep
Limiation : hardware